## Slide 1
AUTOPARK
IoT Based Smart Parking System
A NEXT-GEN
PARKING SOLUTION

## Slide 2: Urban parking congestion, largely driven by rising vehicle density, causes over 30% of city traffic and results in significant economic losses due to fuel waste and delays. Existing systems relying on manual management or RFID face issues like inefficiency, human error, and security risks. To tackle this, we developed AUTOPARK—an IoT-powered smart parking system designed for seamless vehicle authentication, real-time slot tracking, and contactless payments. AUTOPARK enhances security, automates operations, and improves space utilization, making it ideal for scalable deployment in smart cities. This project not only delivered technical improvements but also strengthened our skills in teamwork, problem-solving, and project execution. Abstract

## Slide 3: Contents
• | Problem Statement | 
• | Introduction | 
• | Comparison | 
• | Hardware Layer | 
• | Communication Layer | 
• | Application Layer | 
• | Methodology | 
• | Workflow & Algorithms | 
• | Implementation & Results | 
• | Website Implementation | 
• | Prototype Illustration | 
• | Challenges & Limitations | 
• | Future Scope | 
• | Conclusion | 
• | References | 

## Slide 4: Problem statement
Urban areas face severe parking inefficiencies, causing traffic congestion and revenue losses.
RFID-based systems, while more secure, suffer from high costs, cloning risks, and maintenance issues.
Manual systems are prone to human errors, unauthorized parking, and fraud.

## Slide 5: Introduction To address the mentioned problems, we present AUTOPARK, an IoT-driven smart parking solution designed for automation, affordability, and scalability. It uses ESP8266 microcontrollers, IR sensors, servo motors, and QR code-based authentication to fully automate entry, exit, slot monitoring, and billing. Users scan a unique QR code for access, with real-time slot availability shown on OLED displays and a cloud dashboard. Exit is similarly automated, with fees calculated based on parking duration. This reduces manual intervention, unauthorized access, and operational costs.

## Slide 6: Comparing with existing systems
Cost Analysis:
RFID vs. IoT
Scalability
Efficiency
Metrics
Response Time:
IoT: 45% faster entry/exit
Automation: Higher in IoT-based systems
Security: RFID more secure unless IoT uses enhanced encryption
RFID: Costly, infrastructure-heavy for dense areas
IoT: Easily scalable; modular expansion
Real-world examples: Madrid, Tokyo — 60% better space utilization with AI
RFID: $50–$70 per vehicle; high maintenance (tag replacement, recalibration)
IoT (ESP8266 + IR sensors): ~30% lower cost; minimal maintenance

## Slide 7: Hardware Layer (1/2)
IR Sensor Module
Detects vehicle presence (range: 2–30 cm)
Operates at 3.3V–5V with <1 ms response time
Real-time parking slot occupancy detection
OLED Display Module
0.96” or 1.3” screen, 128x64 resolution
Supports I2C/SPI interfaces
Displays real-time parking data and animations
Servo Motor Module
Controls entry/exit gates
Torque: 2.5–10 kg/cm | Voltage: 4.8V–6V
Rotational range: 0–180° for barrier movement
Triggered after QR code verification
Connectors, Adapter & LEDs
Connectors: Insulated copper wires for stable signals
DC Adapter: 5V regulated power for system components
LEDs: Green = Available, Red = Occupied slots
Parking Slot Detection System
1 ESP8266 + 4 IR sensors + OLED display
Detects and shows real-time slot availability
Pin configuration mapped to GPIO pins (refer to table)
Gate Control System Pin Configuration
ESP8266 connected to servo motor for gate control
Dedicated GPIO pins for servo and IR input
Ensures responsive gate operation

## Slide 8: Hardware Layer (2/2)
ESP8266 Microcontroller Module
Acts as central control unit
Wi-Fi-enabled 32-bit RISC processor (80–160 MHz)
64 KB SRAM, 4 MB Flash Memory
Supports Wi-Fi 802.11 b/g/n with WPA/WPA2
Ultra-low power consumption; ideal for IoT
AUTOPARK OLED Animation
Displays animation of approaching car
Branding text: “Next-Gen Parking System”
Shows live status of parking slots
Circuit Diagram & Dual ESP8266 Setup
ESP8266 (1): Handles display + slot detection
ESP8266 (2): Manages gate control + web communication

## Slide 9: Communication layer
Enables seamless data exchange between hardware, cloud, and users
01
Ensures secure and real-time system responsiveness
02
Wireless Communication
Uses Wi-Fi (802.11 b/g/n) via ESP8266 module
Supports HTTP requests (web communication)
Uses MQTT protocol for low-latency messaging
Ensures data security with TLS/SSL encryption
Provides real-time, efficient data transfer
Cloud Integration
Supports Firebase / AWS for cloud database storage
Real-time sync of parking slot data to users
Uses JSON format for efficient data handling
Optimized protocols to reduce bandwidth and latency
Ensures fast, secure, and scalable communication

## Slide 10: Application layer
Manages user interface, data processing, and analytics
01
Users register via web portal → Unique QR code generated
02
Admin scans QR code to authorize entry/exit
03
Servo motor triggered on successful verification
04
Entry/exit timestamps recorded for billing
05
IR sensors monitor slots in real time
06
OLED display & cloud dashboard show live slot status
07
Auto billing system calculates charges based on duration
08
Supports digital payments: Credit Card, UPI, Wallets
09
Web app shows: slot availability, transaction history, cost estimate
10
User Site: autoparkltd.netlify.app
11
Admin Site: autoparkadmin.netlify.app
12

## Slide 11: Methodology
Step 1: Requirements Gathering
  Urban parking needs analysis
  Defined scope: real-time monitoring, automation, reduced congestion
Step 2: Hardware Design & Selection
  ESP8266 for Wi-Fi and low power use
  IR sensors for vehicle detection
  OLED display for slot status
  Servo motors for automated gate control
  LEDs and power modules for reliability
Step 3: Software & Cloud Integration
  Web app for user/admin interface (HTML, CSS, JS)
  Firebase/AWS for real-time data sync and storage
  Secure API-based communication
Step 4: Integration & Testing
  Hardware-software sync (IR, OLED, QR, servo)
  Functional + integration testing for performance
Step 5: QR Code Authentication
  Unique, encrypted QR for each user
  HTTPS-secured admin scanning and access control
Step 6: Real-Time Slot Detection
  IR sensors → ESP8266 → Cloud → Web + OLED update
Step 7: Billing & Payment System
  Entry/exit time tracking
  Auto bill generation with UPI, card, wallet payments
Step 8: Final Testing & Deployment
  Real-world deployment + continuous monitoring
  User feedback loop for refinement and optimization
01
08
07
06
05
04
03
02

## Slide 12: Workflow

## Slide 13: Algorithms (1/2)
Algorithm of User Registration Process
Start
User visits AUTOPARK website
Select "Signup"
Enter information: Name, Email, Vehicle Number
Submit form
Check if information is valid:
If No: Show "Invalid Input", Retry
If Yes: Proceed
Create account
Confirm email
Check if email is verified:
If No: Resend email, Retry
If Yes: Proceed
Generate unique QR Code
End
Algorithm of Parking Slot Detection
Start
User logs in to AUTOPARK website
Retrieve parking slot information
Detect slots
Check if slots are found:
If No: Retry slot detection
If Yes: Proceed
Check if slots are available:
If No: Show "All slots are full", End
If Yes: Proceed
Show empty slots
User parks and scans QR Code
Confirm parking
Show success
End

## Slide 14: Algorithms (2/2)
Algorithm of Entry-Exit and Billing System
Start
User enters gate
Scan QR Code
Check if QR Code is valid:
If No: Show error, Retry
If Yes: Open gate
User parks vehicle
Start time counter
User exits vehicle
User exits parking
Scan QR Code again
Check if QR Code is valid for exit:
If No: Show error, Retry
If Yes: Open exit gate
End time counter
Generate bill
End
Algorithm of Hardware Implementation
Start
Detect vehicle using IR sensor
Wait for IR signal
Check if vehicle is present:
If No: Update status: Slot available
If Yes: Update status: Slot occupied
Send slot status data to ESP8266
Use Blynk API to update AUTOPARK website
End

## Slide 15: Implementation
Hardware Integration
Components: ESP8266, IR sensors, OLED, servo motors, 5V DC power supply
Arduino IDE used for microcontroller programming
Servo motors control gates based on QR code authentication
Network & Cloud Connectivity
ESP8266 enables Wi-Fi data transfer
Firebase used for real-time database and synchronization
Secure API endpoints manage communication between system and cloud
Web Application Development
Built using HTML, CSS, JS, Node.js, Express.js
Functions: user registration, QR generation, slot monitoring, online payment
Security Measures
QR codes encrypted
HTTPS enforced for all data transfers
Anomaly detection alerts for suspicious activities
System Testing
Functional, load, and network security tests conducted
Performance evaluated for multi-user scenarios

## Slide 16: Results
System Performance
Real-time vehicle detection with <1 sec response time
Smooth gate automation using QR authentication
OLED displays show live parking status
Cloud & Admin Efficiency
Remote access to parking records and transaction logs
Centralized dashboard for monitoring and reporting
Security and Stability
Encrypted QR codes prevent unauthorized access
HTTPS and anomaly detection enhance data protection
User Experience
Easy registration, real-time slot updates, secure digital payments
Positive feedback for system speed and reliability
Improvement Areas
Occasional sync delays due to network issues
Future updates: edge computing & AI-based predictive analytics

## Slide 17: Registration Process of Autopark

## Slide 18: Email Verification Process of Autopark

## Slide 19: Login to Autopark

## Slide 20: Autopark Log Entry Page

## Slide 21: Autopark Log Exit Page

## Slide 22: Autopark Admin Interface

## Slide 23: Autopark Payment Gateway

## Slide 24: Prototype Illustration

## Slide 25: Challenges and limitations
Network Reliability & Latency
02
Challenge: Unstable Wi-Fi, latency issues
Implementation: Use of mesh networks & hybrid communication models
Cost & Maintenance
05
Challenge: High setup cost for small entities
Implementation: Open-source platforms & predictive maintenance tools
Sensor Accuracy & Environment
03
Challenge: Weather interference, dust accumulation
Implementation: Regular maintenance & adaptive calibration
User Adoption
06
Challenge: Resistance from low digital literacy regions
Implementation: Intuitive UI/UX & awareness campaigns
Future Vision
AI-driven slot reservation, blockchain security, voice navigation
Infrastructure & Deployment
01
Challenge: Retrofitting outdated facilities; high initial cost
Implementation: Modular hardware design & phased deployment
Security & Privacy
04
Challenge: QR code forgery, data breaches
Implementation: End-to-end encryption & multi-factor authentication

## Slide 26: Future Scope
Integration with Payment Systems
Mobile App Development
Advanced sensors and machine learning
Real time parking slot reservation
Integration with smart city platforms

## Slide 27: Conclusion
Revolutionizing Parking with IoT:
  Combines ESP8266 and Blynk app for real-time parking management.
  Enhances convenience, efficiency, and user accessibility.
Scalable and Sustainable:
  Adaptable for residential, commercial, and public parking needs.
  Supports smart city goals by reducing fuel consumption and emissions.
Future-Ready Innovation:
  Opportunities to integrate AI for predictive parking and optimization.
  Enhanced data security measures to protect user information.
Impact:
  AUTOPARK is a step toward sustainable, efficient, and intelligent urban mobility.

## Slide 28: References
Javaheri, Atusa, et al. "Evaluating Impact of Smart Parking Systems on Parking Violations." IEEE Access (2024). https://doi.org/10.1109/ACCESS.2024.3503513
[24] Jenila, C., and K. Harshan. "IoT-based Smart Parking System: Hardware-Centric Approach for Addressing Urban Parking Challenges." 2024 2nd International Conference on Networking, Embedded and Wireless Systems (ICNEWS). IEEE, 2024. https://doi.org/10.1109/ICNEWS60873.2024.10731004
[25] Piruthiviraj, P., et al. "IoT based Vehicle Monitoring System for Safety Standards in Smart Cities." 2024 4th International Conference on Pervasive Computing and Social Networking (ICPCSN). IEEE, 2024. https://doi.org/10.1109/ICPCSN62568.2024.00110
[27] Araújo, Anderson, et al. "Reliability analysis of an IoT-based smart parking application for smart cities." 2017 IEEE International Conference on Big Data (Big Data). IEEE, 2017. https://doi.org/10.1109/BigData.2017.8258426
[39] Alam, Md Rokibul, et al. "A Survey on IoT Driven Smart Parking Management System: Approaches, Limitations and Future Research Agenda." IEEE Access 11 (2023): 119523-119543. 10.1109/ACCESS.2023.3327306

## Slide 29: Thank you
Submitted by:
JENIFA KHATUN | (ROLL NO: 18700321048)
JEET CHATTERJEE | (ROLL NO: 18700321084)
ARCHISHMAN DUTTA | (ROLL NO: 18700321049)
ADDRI KIRAN DEY | (ROLL NO: 18700321044)
ABHIPSA CHAKRABORTY | (ROLL NO: 18700321060)
Under the supervision of PROF. (Dr.) DIPSIKHA DAS